VIN: 1GTHK291012345678

Year: 2002

Make: GMC

Model: 2500HD

Configuration: Extended Cab Long Box

Drive: Selectable 4x4

Engine: 6.6L (403Cu.In.) Duramax Turbo Diesel (LB7 Federal Emissions)

Transmission: Allison 1000 5spd Automatic

Transfer Case: New Venture Gear 263XD (Electric Shift)

Front Axle: AAM 925 IFS version

Rear Axle: AAM 1150 with Gov-Loc

Tires: LT265/75R16 Rear: 60PSI   Front: 60PSI   Lug Nut Torque: 140lb-ft

Windshield Wipers: 22” “J”-Hook, Both sides

Batteries(x2): 78 Series, 1000CA/880CCA Side screw in terminals

Fluids

| Oil | Trans | Coolant | P/Steering | Axles | Brake | T-Case | Grease |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 15w40 | Dex III | DexCool | Univ./Steer. | 75W90Syn | DOT 3 | Dex III | Universal |

Filters

| Oil | Fuel | Air | Trans(Spin) | Trans(Internal) | Cab |
| --- | --- | --- | --- | --- | --- |
| 7202 | 3960 | 6678 | 7701 | 8662 | 4814 |

Capacities (Quarts)

| Oil | Trans(Spin) | Trans(Full) | Diff.(Front) | Diff(Rear) | TCase | Coolant |
| --- | --- | --- | --- | --- | --- | --- |
| 10 | 0.5 | 7.5 | 2 | 4 | 2 | 20 |

Bulbs

| Headlamp (Low) | Headlamp (High) | Park/Signal (Front.) | Stop/Tail/Signal (Rear) | Reverse | DRL | 3rd Brakelight | Side Marker |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 9006 | 9005 | 3157NA | 3157SA | 3157SA | 4114LL | 921 | 194 |